## Slide 1: DOB를 이용한 외발자전거 제어
기계항공공학부 우주항공공학전공
2019-11545 이종안

## Slide 2: Model
ψ, θ, γ: z-x-y Euler angles
x_G, y_G: 바퀴의 위치
ϕ, α, β: 각 바퀴가 돌아간 각도
σ : Pseudovelocities
Xincheng Cao et al. “Autonomous unicycle: modeling, dynamics, and control”. In: Multibody System Dynamics (2023), pp. 1–34.

## Slide 3: Non-linear Model
The state and input
Wheel Torque

## Slide 4: Linearized Model
를 평형점으로 하여 선형화(단 w_b*, w_s*=0)
Form

## Slide 5: Normal Form
All three have a relative degree of 2
Each input has a matching output y
Zero dynamics do not affect the output

## Slide 6: Nominal Plant Controller
Problem: System Not Controllable(rank(Co)=11)
Still stabilizable, so Okay!
Nominal Plant Controller: PD controller of the Euler Angles!
Stability with eigenvalues of x at LHP and z at 0

## Slide 7: MIMO DOB
MIMO DOB inherently uses separate Q filters for each y
 Use independent Q filters to estimate x!
Juhoon Back et al. “An Inner-Loop Controller Guaranteeing Robust Transient Performance for Uncertain MIMO Nonlinear Systems”. In: IEEE Transactions on Automatic Control (2009)

## Slide 8: MIMO DOB
Inverse Plant used to estimate u from x
 Since each u is independent, use the SISO approach

## Slide 9: Simulation
Initial position of (1,1,1) rad or 57.3°
DOB decreased overshoot (important to not go over 0.5π=1.57)

## Slide 10: Conclusions
Initial PD controller was too good  affect of DOB not apparent
Use a controller without a derivative term next time
Theoretical stability not yet proven